1. Introduction
2. Prerequisites
3. Overview
4. Building Code
  1. Libraries
  2. Programs
5. Summay of Environment Variables That Control Build Behavior

1 Introduction

This build system is based on the tool "cmake" version 2.8.8.
All syntax in build description files mentioned below conforms to the rules for cmake CMakeList.txt files as found in the cmake documentation.

2 Prerequisites

One must have their bash shell environment set up via the ACC environment setup procedure described here: https://wiki.lepp.cornell.edu/lepp/bin/view/ACC/ACL/DevelopmentEnvironmentSetup

3 Overview

The build system will compile C, C++, and Fortran (77,90,95,2003) source code into object code and link into libraries and/or executables (programs).

To control how a project's source code is built one composes or edits an existing file named CMakeLists.txt. This file must appear in a project directory in order for the build system to recognize that directory as project that can be built.

The system operates within some directory organization requirements. The base directory wherein one or more project directories are located will be referred to as <DIR>.
The project directory in question will be referred to as <PROJ_DIR> = <DIR>/<PROJECT>.
- Within <PROJ_DIR> there may be one or more subdirectories containing one or more source code files in any of the languages mentioned above.
- Within <PROJ_DIR> there may be one or more subdirectories containing header files necessary for compilation.

4 Building Code

  1. Libraries

Provided a CmakeLists.txt build description file exists in the project directory that you wish to build, invoking the command mk will build a “production” binary which is suitable for everyday running. The command mkd will build a “debug” binary that contains debugging symbols for use in an interactive debuuger.

The object and other support files are kept in a separate build tree automatically created within the project directory called production or debug, depending on the build type requested.

mk clean will clean the object files and binaries of the production build type and mkd clean will do the same for the debug build type.

To control the building of a library, create or copy a file named CmakeLists.txt into <PROJ_DIR>. An example CmakeLists.txt file is shown and annotated here.
The gray text is boilerplate and must appear verbatim. The remaining sections are meant to be modified by the user to configure the details of the build. This example is used to build the libcesrv.a static library file and to allow for building the cesrv_cl program

set(LIBNAME cesrv)
cmake_minimum_required(VERSION $ENV{ACC_CMAKE_VERSION})

find_package(X11)

set(INC_DIRS
  ${X11_INCLUDE_DIR}
  ../include
  ../CesrBPM/include
  include
)

set(SRC_DIRS
  code
)

set(DEPS
    mpm_utils
    nonlin_bpm
    cesr_utils
    bmad
    sim_utils
    CesrBPM
    cbpmfio
    mpmnet
    recipes_f-90_LEPP
    cbi_net
    c_utils
    pgplot
    xsif
    forest
)

set(EXE_SPECS cesrv.cmake)

include($ENV{ACC_BUILD_SYSTEM}/Master.cmake)

INC_DIRS holds the list of directories in <PROJ_DIR> to search for include files.
SRC_DIRS holds the list of directories in <PROJ_DIR> that hold C, C++, and/or Fortran source code files to compile.
DEPS holds the list of in-house libraries that the software being built depends upon. This ensures that the necessary code in the project gets rebuilt in the event a local dependency library is modified.
EXE_SPECS holds the list of build specifications needed for producing one or more programs. See below for details.

  1. Programs
To control the building of an executable, create or copy a file named after the program to produce into <PROJ_DIR>. In this example, the supplementary build description file is called cesrv.cmake which will be used to produce the executable file cesrv_cl.

set (EXENAME cesrv_cl)
set (SRC_FILES
  program/cesrv_cl.f90
)

set (LINK_LIBS
  cesrv
  mpm_utils
  nonlin_bpm
  cesr_utils
  bmad
  sim_utils
  cbpmfio
  CesrBPM
  mpmnet
  recipes_f-90_LEPP
  cbi_net
  pgplot
  xsif
  forest
  -Bdynamic /usr/lib64/libX11.so
  readline
  curses
  stdc++
)

EXENAME is the name of the program file to be built.
SRC_FILES is a list of file paths (relative to <PROJ_DIR>) of the source files containing the program's main routine and other functionality that is not to be included in a library.
LINK_LIBS is the list of additional libraries, if any, that provide functionality to the program being built.

To actually create the executable upon invocation of the mk command, a session variable can be set to in the user's environment called ACC_BUILD_EXES. Several affirmative values of this variable will be honored as per the cmake documentation. A short list of values that will result in the intended behavior is “ON”, “TRUE”, “Y”, “YES”, “1”. This allows the creation of all executables for which <executable>.cmake files have been created and for which references are present in the
SET (EXE_SPECS <spec1> <spec2>...) line.

Alternatively, if the ACC_BUILD_EXES variable is not set affirmatively, individual executables can be created by using the name of their target after the mk[mkd] command. Program target names have an “-exe” appended to them.
I.e. mk <program_name1>-exe